## Slide 1: Delay, Loss, and Throughput
CPSC 3600

## Slide 2: Review Questions
R1: What is the difference between a host and an end system? List several different types of end systems. Is a web server an end system? R3: Why are standards important for protocols? R5: Is HFC transmission rate dedicated or shared among users? Are collisions possible in a downstream HFC channel? Why or why not? R8: What are some of the physical media ethernet can run over? R11: Suppose there is exactly one packet switch between a sending host and a receiving host. The transmission rates between the sending host and the switch and between the switch and the receiving host are R1 and R2, respectively. Assuming that the switch uses store-and-forward packet switching, what is the total end-to-end delay to send a packet of length L? (ignore queuing, propagation delay, and processing delay) R14: Why will two ISPs at the same level of the hierarchy often peer with each other? How does an IXP earn money?

## Slide 3: What are potential sources of packet delay? Packet loss?

## Slide 4: Sources of Delay
Four sources of delay at a given node/router
  Processing time (checking if packet was rcvd OK, where it goes)
  Queueing delay (waiting for the output link to be available)
  Transmission delay (time required to push out the packet onto link)
  Propagation delay (time to travel across the link)

## Slide 5: Sources of Delay

## Slide 6: Nodal Processing Delay
Delay is negligible, typically on the order of microseconds
Delay comes from checking for bit-level errors and routing the packet

## Slide 7: Queuing Delay
Variable delay, ranges from 0 to ∞, depends on how many other packets are in the queue
In practice, ranges from microseconds to milliseconds

## Slide 8: Transmission Delay
The amount of time required to push a packet out onto the transmission medium
Delay related to:
  L, length of packet
  R, transmission rate of link (e.g. 100 Mbps)
Actual delay = L/R
Typical delays in the range of milliseconds to microseconds

## Slide 9: Propagation Delay
Depends on the medium (e.g. copper wire, fiber optic) and the distance
  Speeds usually range from 2*10^8 to 3*10^8
Delay = distance / speed
  E.g. 2*10^8 m/s in a copper link of 2000 km = 0.01 ms

## Slide 10: Propagation Delay
Unusual medium defined in RFC 1149
  IPoAC - IP over Avian Carriers
  Has been actually implemented, sent 9 packets 5 km
  Avg delay was 5222806 ms
  Potential for very high throughput if pigeons carry high density SD cards, but long propagation delay

## Slide 11: Propagation Delay
Unusual medium defined in RFC 1149
  IPoAC - IP over Avian Carriers
  Has been actually implemented, sent 9 packets 5 km
  Avg delay was 5222806 ms
  Potential for very high throughput if pigeons carry high density SD cards, but long propagation delay
  Higher risk of dropped packets

## Slide 12: Transmission + Propagation Delay
Consider a caravan of cars traveling on a toll road
  1 caravan of 10 cars = 1 packet with 10 bits
  Caravan can’t start going through until all the cars have arrived
Toll booth takes 12 seconds to service a car (dtrans)
Cars “propagate” at 100 km/h (dprop)

## Slide 13: Transmission + Propagation Delay
Consider a caravan of cars traveling on a toll road
  1 caravan of 10 cars = 1 packet with 10 bits
  Caravan can’t start going through until all the cars have arrived
Toll booth takes 12 seconds to service a car (dtrans)
Cars “propagate” at 100 km/h (dprop)
How long till caravan is lined up at the 2nd toll booth? 62

## Slide 14: Transmission + Propagation Delay
Toll booth takes 1 minute to service a car (dtrans)
Cars “propagate” at 1000 km/h (dprop)

## Slide 15: Transmission + Propagation Delay
Toll booth takes 1 minute to service a car (dtrans)
Cars “propagate” at 1000 km/h (dprop)
How many cars will still be at the first booth when the first car arrives at the second?

## Slide 17: How can we extend this analogy to also include queuing delay?
Notes: Put other caravans on the road, representing other packets. You’ve got to wait at the toll booth for the earlier caravan to get through

## Slide 18: Queueing delay
Queueing delay = R/L
  R = link bandwidth (bits/sec)
  L = packet length (bits)
a = average packet arrival rate
L*a/R ~ 0 → avg queueing delay is small
L*a/R ~ 1 → avg queueing delay is large
L*a/R > 1 → avg queueing delay is ∞
L*a/R ~ 0
L*a/R ~ 1
L*a/R > 1

## Slide 20: Example of Queuing Delays
https://media.pearsoncmg.com/aw/ecs_kurose_compnetwork_7/cw/content/interactiveanimations/queuing-loss-applet/index.html

## Slide 21: “Real” Internet delays and routes
What do “real” Internet delays look like?
The traceroute program measures delay from source to router along end-to-end paths to the destination
For all i:
  Send three packets that will reach each router i along path towards destination
  Router i will return packets to dender
  Sender times interval between transmission and reply
http://traceroute.org/

## Slide 22
Traceroute to http://www.clemson.edu (130.127.204.30), 30 hops max, 40 byte packets 1 core-87-router (128.112.128.2) 1.103 ms 0.643 ms 0.453 ms 2 border-87-router (128.112.12.142) 0.947 ms 0.718 ms 0.653 ms 3 local1.princeton.magpi.net (216.27.98.113) 1.944 ms 2.771 ms 1.914 ms 4 216.27.100.18 (216.27.100.18) 2.183 ms 2.162 ms 2.027 ms 5 et-1-1-0.4079.rtsw.wash.net.internet2.edu (162.252.70.119) 5.796 ms 5.933 ms 5.639 ms 6 et-5-0-0.4079.rtsw.rale.net.internet2.edu (162.252.70.120) 10.592 ms 10.635 ms 14.369 ms 7 205-186-224-49.generic.sclightrail.net (205.186.224.49) 16.098 ms 16.294 ms 16.170 ms 8 * * * 9 205-186-62-89.generic.c-light.net (205.186.62.89) 19.316 ms 19.462 ms 20.118 ms 10 205-186-62-88.generic.c-light.net (205.186.62.88) 19.315 ms 19.799 ms 19.000 ms 11 130.127.3.186 (130.127.3.186) 20.691 ms 20.787 ms 130.127.3.185 (130.127.3.185) 20.982 ms 12 130.127.3.152 (130.127.3.152) 20.321 ms 20.248 ms 130.127.3.64 (130.127.3.64) 20.626 ms 13 130.127.3.102 (130.127.3.102) 20.676 ms 130.127.204.30 (130.127.204.30) 20.641 ms 130.127.3.102 (130.127.3.102) 20.733 ms

## Slide 23: Class Activity
Go to http://traceroute.org/
Who can find the shortest hop delay? The longest hop delay?

## Slide 24: Packet Loss
Packet queues have finite capacity
Possible to have a packet arrive and not have space for it
  Packet is dropped (i.e. lost)
Lost packet can be retransmitted by previous node, by the origin node, or not at all
Packets can also be dropped if they are corrupted in transit

## Slide 25: Throughput
Throughput: the rate (bits/time unit) at which bits are transferred between sender and receiver
  Instantaneous throughput: rate at a given point in time
  Average throughout: rate over longer periods of time

## Slide 26: Throughput
What is the average end-end throughput? (Rs < Rc)

## Slide 27: Throughput
What is the average end-end throughput? (Rs > Rc)

## Slide 28: Throughput
Bottleneck link: the link on the end-to-end path that constrains end-to-end throughput
Per-connection end-end throughput: min(Rc, Rs, R/10)
In practice, Rc or Rs are usually the bottleneck

## Slide 29
Suppose you need to deliver 40 terabytes of data to your co-workers in Atlanta (200 km). You have an available 100 Mbps dedicated link for data transfer.
Alternatively, your friend raises homing pigeons and would be willing to let you borrow one. You have a single 1 TB SD card you can strap to the pigeon. Assume pigeons can fly 1000 km per day and that it takes no time to copy to/from the SD card.
What would be faster?
Dedicated 100 Mbps link
Pidgeon

## Slide 30
Suppose you need to deliver 40 terabytes of data to your co-workers in Atlanta (200 km). You have an available 100 Mbps dedicated link for data transfer.
Alternatively, your friend raises homing pigeons and would be willing to let you borrow one. You have a single 1 TB SD card you can strap to the pigeon. Assume pigeons can fly 1000 km per day and that it takes no time to copy to/from the SD card.
Roughly how long would it take to use the dedicated link?

## Slide 31
Suppose you need to deliver 40 terabytes of data to your co-workers in Atlanta (200 km). You have an available 100 Mbps dedicated link for data transfer.
Alternatively, your friend raises homing pigeons and would be willing to let you borrow one. You have a single 1 TB SD card you can strap to the pigeon. Assume pigeons can fly 1000 km per day and that it takes no time to copy to/from the SD card.
Roughly how long would it take to use the pigeon?

## Slide 32
What is the biggest source of delay for the 100 Mbps dedicated link?
Dnodal
Dqueuing
Dtransmission
Dpropagate

## Slide 33
What is the biggest source of delay for the pigeon?
Dnodal
Dqueuing
Dtransmission
Dpropagate

## Slide 34: Before Next Class
Read Section 1.5, 2.1
Complete 2 of the following problems
  R16, R18, R19
Complete 2 of the following problems
  P6, P7, P12, P20