## Slide 1: 1) The geochemically scarce metals 2) Mining Methods

## Slide 2: Scarce metals
Used in small amounts
Can control the properties of alloys of the abundant metals
<0.1 % average abundance in crust
>30 scare metals are mined
Fill a wide, varied range of needs
  Distribution of electricity, phones, radio, TV, cars, planes, rockets, computers, internet…
  keep our modern society running efficiently and effectively
Average abundance of elements in continental crust
Notes: Some as little as 1/1,000,000th of a percent average crustal abundance

## Slide 3: Scarce metal occurrence
How are the scarce metals distributed in MOST of Earth’s crust?
  Present in common minerals by atomic substitution
  eg. Ni can substitute for Mg in olivine (Mg2SiO4)
BUT – the number of scarce metal atoms that can substitute into common minerals is limited
When that limit is exceeded,
we have reached saturation of that metal
Atomic substitution
Common mineral
Notes: Saturation of the solid solution – this is when you can form minerals of the scarce metals

## Slide 4: Ore minerals of the Scarce Metals = minerals in which scarce metals are key component of the mineral,
Formed when you reach saturation of the scarce metal in common minerals
 RARE circumstances (ore deposits!)
Cut-off grades vary – e.g…
  0.0001% gold
  1-3% zinc
  40% chromium and manganese
Concentration factors required to reach saturation can be enormous
Notes: not just present in small quantities, substituting for other common metals
Concentration factors: Mercury 12,500 x greater than average crustal abundance
Thus ore deposits of scarce metals tend to be small and scarce relative to the abundant metal deposits

## Slide 5: Classification by usage
Ferro-alloy metals
Base metals (nonferrous metals)
Precious metals
Special metals
Notes: 1 – primarily used to alloy with iron
2 – purposes other than alloying with Fe
3 – non-reactive (thus corrosion resistant
4 – range of special properties

## Slide 6: Chapter 8 – useful reading – Will scan and post this chapter
Details the most important scarce metals
Systematically describes
  Uses
  Geologic occurrence
  Production and reserves
I think it is quite interesting stuff, but I want you to read it on your own
  Familiar with the different important scarce metals
  Their geologic occurrence
  And their most important uses – how do they impact our lives?

## Slide 7: A few interesting tidbits to highlight
Vanadium – Substitutes for Fe and Mg
  LII, weathering – oxidizes to very soluble form
  Substitute into cells in organic matter (e.g. hemoglobin and chlorophylls) – appear as “cages” with V in center called porphyrins
    Thus extractable from coal and Tar (heavy oil)
Chlorophyll

## Slide 8: A few interesting tidbits to highlight
Nickel – Liquid immiscibility in mafic magmas
  When magma starts to cool, minerals crystalize because the magma becomes saturated in those mineral’s chemical constituents
  Magma may become saturated in a compound, but still be hotter than the melting temperature of that compound
  The compound may separate out into immiscible liquid blebs (like oil and water)
Notes: Pyrrhotite does this a lot

## Slide 9: A few interesting tidbits to highlight
Sudbury Ontario – large Ni and Cu mine
Formed from a large meteorite impact!

## Slide 10: A few interesting tidbits to highlight
Cobalt – German miners
  Arsenic bearing silver-cobalt ores
  Arsenic gas caused ulcers on bodies of miners
  Miners thought they were caused by silver stealing goblins called Kobolds who replaced good silver with useless cobalt-arsenides

## Slide 11: A few interesting tidbits to highlight
The tungsten ore Sheelite glows bright blue under UV light!
Formed in veins
Important use is for making tungsten carbide, which has hardness approaching that of diamond

## Slide 12: A few interesting tidbits to highlight
Copper – LOTS of deposits
Most important ores are sulfide minerals
We talked about Porphyry deposits – formed by hydrothermal fluids associated with sub-volcanic igneous intrusions
 Role of underground steam explosions in this process
Notes: Water content of magma increases as non-hydrous phases crystalize – water content increases
These magmatic derived fluids can cause steam explosions underground – shatters the rocks, and then minerals (including sulfide minerals) can crystalize in those cracks forming veins
Veins are too scattered to mine individually, so we crush up the whole body of rock and leach out the copper

## Slide 13: A few interesting tidbits to highlight
Gold
Low grade deposits:
  Mostly those deposit types that form via hydrothermal fluids
Veins
Placer deposits (e.g. Witwatersrand in South Africa)
Notes: Witwatersrand = delta conglomerates – original source of gold long eroded away

## Slide 14: Mining Methods
Surface
  Open Pit
  Strip/Mountaintop Removal
Underground

## Slide 15: Surface Mining
Accounts for 2/3 of world’s mineral production
Especially the production of sand and gravel, crushed stone, and phosphates, coal, copper, iron, and aluminum
This includes open pit mining and strip mining

## Slide 16: Advantages of Surface Mining
Safer
Less expensive
Fewer complications with water, bad air, electricity and falling rock than underground mines
Less regulation than underground mines

## Slide 17: Bingham Copper Mine, Utah
Deepest open pit copper mine in the world!

## Slide 18
Almost three miles wide and a half mile deep.

## Slide 19
Notes: Describe what surface mining is – dig out pit, process ore, all non ore rock that is removed plus the waste rock after ore processing goes in tailings piles

## Slide 20: Bingham Tailings Waste Pile

## Slide 21: Why an Open Pit?
Open pits are economical where:
  large tonnages of reserves are involved
  high rates of production are desired
  overburden is thin enough to be removed

## Slide 22: Quarry
Quarry is an open pit mine specifically for excavating building stone
Granite Quarry and Sand Pits

## Slide 23: Strip Mining
Why a strip mine?
Used where material to be extracted forms a flat lying layer below the surface, with minimal overburden
**generally used for coal

## Slide 24: Coal Seam in Road Cut

## Slide 25: Underground Mining
Used to extract a solid mineral resource that is too deep to allow for economic surface extraction
Composed of shafts, (horizontal) adits and inclines
Potential Issues
Ventilation is big concern here – many smaller shafts needed for ventilation
Flooding can be a problem
Temperature – too hot to work
Mine collapse

## Slide 26: Underground Mining

## Slide 27: Underground Mining Methods
Method used to mine depends upon type of deposit – shape, size, grade
Drilling and Blasting is used in most mines - then removal with automatic diggers onto rail cars or elevators to the surface
Coal mines often use continuous mining machines

## Slide 28: Room and Pillar Method
Implication: you leave some of the ore to hold up the cavern

## Slide 29: Robbing the Pillars
This was done in coal mines when the
high grade coal was exhausted

## Slide 30: Long Wall Mining: What you mine you let collapse

## Slide 31: Long Wall Mining: What you mine you let collapse
In the photo on the right note the hydraulic roof supports above and behind the miner

## Slide 32: Strength of the rocks and Mining
The strength of the rocks being mined is a large determinant in the mining method and type of mining cavern produced
Sedimentary rocks are usually not as strong – roof collapse is a big concern

## Slide 33: Underground Mining Dangers
Rock falls – collapsing roofs
Poisonous and combustible gases – no use of gasoline in mines
Methane generation – coal mines