## Slide 1
CPU
cache
memory
controller
keyboard
display
controller
disk
controller
Computer Systems
Here is a diagram of a simple computer system:
(this diagram will be the one needed for exams)
bus

## Slide 2
DRAM memory
Backside = L2 cache =
South-Bridge Controller (I/O hub)
North-Bridge Controller (memory hub)
monitor
Graphics accelerator (with local memory)
Computer Systems
A current consumer PC uses multiple buses
(this diagram is *not* required for exams)
CPU core
FSB
800 MHz
AGP
1 Gbit Ethernet
Serial ATA
disk
CD/DVD
10 Mbit Ethernet
PCI bus
Parallel ATA
South-Bridge has dedicated ports for legacy devices, such as Q Mouse keyboard, floppy; also has serial and parallel ports
South-Bridge typically contains flash eprom holding the BIOS, real-time clock, CMOS memory, w\ independent battery backup.

## Slide 3: Computer Components
input - keyboard, mouse, scanner, ...
output - display, printer, sound, ...
CPU == central processing unit == processor composed of two parts:
  datapath (temporary memory, called registers, and function units)
  control logic (sequencing of datapath actions)
different instruction sets:
      Intel IA32 (x86), Apple/IBM/Motorola PowerPC, Sun SPARC, ARM, ...
      common instructions include add, subtract, jump, ...

## Slide 4
  memory
    multilevel hierarchy due to cost vs. speed tradeoffs
      fastest and most expensive --> CPU registers
              cache (perhaps multiple levels)
              main memory
      slowest and least expensive -> long-term storage
Computer components (cont’d)

## Slide 5
  memory
    cache and main memory are made of RAM - random access memory
      DRAM - dynamic RAM - most main memories
      SRAM - static RAM - fast and expensive, used for caches
    ROM - read-only memory (holds initial "bootstrap“ loader program and basic I/O programs)
Computer components (cont’d)

## Slide 6
  long-term storage - so slow that it is treated as I/O
    floppy disk
    hard disk
    CD-ROM
    DVD
Computer components (cont’d)

## Slide 7
K (kilo-) = one thousand = 103 ~ 210 m (milli-) = 10-3
M (mega-) = one million = 106 ~ 220 u (micro-) = 10-6
G (giga-) = one billion = 109 ~ 230 n (nano-) = 10-9
T (tera-) = one trillion = 1012 ~ 240 p (pico-) = 10-12
P (peta-) = one quadrillon = 1015 ~ 250 f (femto-) = 10-15
E (exa-) = one quintillion = 1018 ~ 260 a (atto-) = 10-18
main memory size is measured in powers of two, while speed is in powers of 10 (the capacity of most hard disks is measured in powers of ten)
Prefixes for speed, time, and capacity

## Slide 8
note that some folks are now using special binary prefixes to prevent any confusion (http://physics.nist.gov/cuu/Units/binary.html)
Ki (kibi-) = kilobinary = 210
Mi (mebi-) = megabinary = 220
Gi (gibi-) = gigabinary = 230
Ti (tebi-) = terabinary = 240
Pi (pebi-) = petabinary = 250
Ei (exbi-) = exabinary = 260
Prefixes for speed, time, and capacity

## Slide 9
Program translation
    symbolic (i.e., human readable) languages
      high-level language (HLL)
      assembly language – one-to-one (approx.) correspondence with machine insts.
  machine instructions - represented inside the computer in bit (0/1) patterns
  HLL assembly lang machine code(object file or executable)
  ---- --------------- -------------------------------------------
  A = B + C; --> load(B) --> 0000 0010 0010 0100
  add(C) 0000 0001 0010 0101
  store(A) 0000 0011 0010 0011
each moves closer to the bit representation needed by hardware for execution

## Slide 10
Compiler – A translator that translates statements written in a high-level language (HLL) into assembly code, performing various optimizations and register allocations along the way.
Interpreter – A translator that translates and executes all at a single time
Assembler – A program that takes assembly instructions and converts them into machine code that the computer's processor can use to perform its basic operations. The resulting file is called an object file.
Program translation

## Slide 11
Assembly Language
  a statement in an assembly language is called an instruction
  an instruction is composed of
    operation code (opcode)
    operands (names of registers and/or information needed to generate a memory address)
Program translation

## Slide 12
ARM symbolic code -------> address machine code (in hexadecimal)
main:
mov r0, #0x1 0x00000000 0xE3A00001
mov r1, #0x0 0x00000004 0xE3A01000
loop:
cmp r0, #0x5 0x00000008 0xE3500005
beq stop 0x0000000C 0x0A000002
add r1, r0, r1 0x00000010 0xE0801001
add r0, r0, #0x1 0x00000014 0xE2800001
b loop 0x00000018 0xEAFFFFFA
stop:
…
example: ARM assembler

## Slide 13
labels (like “loop" in the previous example) represent symbolic addresses of data and branch targets in the program
each label must be unique (i.e., it must be defined only once)
assembly
symbolic program (human readable) ----------> machine code (binary)
symbolic labels memory addresses
opcodes bit patterns in instructions
operand identification (registers bit patterns in instructions
and memory address info)
immediate operand values (constants) bit patterns in instructions
Assembly Language

## Slide 14: Assembler
Assemblers have a two-pass structure
  instructions can have forward or backward references to labels
  because of forward references, most assemblers use a two-pass assembly structure, since you encounter a "use" before its "definition" and thus cannot immediately translate the label into its memory address

## Slide 15: Assembler
  two-pass structure:
    pass 1 - a) increment a location counter as you read each assembly language statement and b) build the symbol table by collecting label definitions into a symbol table with the corresponding location counter values
    pass 2 - using the symbol table, translate the assembly language statements into machine code

## Slide 16: Forward references
symbolic code | assign addresses using a location counter | translated code (will be represented in binary)
… | 100: … | …
jmp next | 101: jmp next | <jmp op> <addr=103>
… | 102: … | …
next: add x | 103: add x | <add op> <addr=106>
… | 104: … | …
halt | 105: halt | <halt op>
x: .word 16 | 106: 15 | <value=15>
example: the instruction "jmp next" - forward reference to jump target label "next"
the instruction "add x" - forward reference to data label "x"
pass 1 pass 2
----------> ---------->

## Slide 17
  _symbol_table_
  symbol addr
next | 103
x | 106
… | …
New entry when you encounter a label
Table lookup yielding address when you encounter a symbolic label
(note that the symbol table for the assembler holds the address 106 of "x", not its initial value of 15)
alternatively, if you keep all the translated code in memory, you can translate in one pass over the input -- but you must keep a record of all unresolved uses of a label (e.g., the symbol table entry for an as-yet-undefined label points to a linked list of all forward references) and then you backtrack and fix up those uses whenever the definition is encountered