## Slide 1
prior to von Neumann, special memories (e.g., mercury delay tubes, vacuum tubes) were used to store data, and programs were either stored in separate memories or physically wired-up on plugboards
von Neumann is credited with the idea of "stored program" computers, where the program is stored in the same memory as the data and indeed can be treated like data
(the idea originated with ENIAC pioneers Eckert and Mauchly)
von Neumann machine

## Slide 2
random-access, one-dimensional memory (vs. sequential memories)
sequential processing (no pipelining)
stored program, no hardware distinction between instructions and data vs "Harvard architecture" with separate instruction and data memories)
binary, parallel by word, two's complement (vs. decimal, serial-by-digit, sign-magnitude)
instruction fetch/execute cycle, branch by explicit change of PC (vs. following a link address from one instruction to the next)
three-register arithmetic -- ACC, MQ, MBR
von Neumann machine characteristics

## Slide 3
memory contains series of bits grouped into addressable units
  NOTE: binary devices are relatively easy to build – positive feedback drives the device to one of two extreme states and keeps it there, so the decimal storage devices of some old machines were usually four binary devices for which only ten of the sixteen states were used
data is accessed in memory by naming memory addresses (like a big array)
von Neumann machine characteristics

## Slide 4
addresses are consecutive binary integers (unsigned) - this is convenient for addressing arrays and sequentially stepping through a program
bit strings have no inherent data type - can be integer, character string, machine instruction, or just garbage => HARDWARE DOESN'T KNOW DATA TYPE
Von Neumann machine characteristics

## Slide 5
consider
int main(){
int i;
char c = 'a';
printf("%c 0x%x %d\n",c,c,c);
i = c + 1;
printf("%c 0x%x %d\n",i,i,i);
return 0;
}
which prints
a 0x61 97
b 0x62 98
'a' is the (ASCII-encoded) bit string '01100001'; printf() can be told to format this bit string as a character, a hexadecimal number, or a decimal number; also %s can tell printf() to use a bit string as the address of a character string
Von Neumann machine

## Slide 6
note that in C programs, char parameters are passed as 32-bit words and printf() uses the lowest 8 bits for the %c format
int main(){
int i = ( 'a' << 8 ) | 'b';
printf("%c 0x%x %d\n",i,i,i);
i = i + 1;
printf("%c 0x%x %d\n",i,i,i);
return 0;
}
b 0x6162 24930
c 0x6163 24931
NOTE: a few old computers experimented with type fields ("tags") added to memory words to distinguish between data and instruction types
the key point is that programs can be manipulated as data (e.g., think of machine code generated/modified at run time; also compiler, linker,
loader)
von Neumann machine

## Slide 7
A compiler typically type-checks all the variables it uses so that all operations are legal
NOTES:
  a strongly-typed language allows few, if any, implicit type conversions
  in a strong and statically typed language, the compiler declares a compile-time error when types don't match (e.g., C++, Java)
  in a strong and dynamically typed language, the interpreter or other run-time system declares a run-time error when types don't match (e.g., Python)
  because C is generous in using implicit conversions, it is considered weakly-typed with static (compile-time) type checking
von Neumann machine

## Slide 8
accumulator machine – as discussed earlier.
stack machine - operands are on stack, push from memory/pop into memory
load/store machine - computational instructions operate on general registers and load/store instructions are only ones that access memory
Varieties of processors

## Slide 9
Accumulator Machine
CPU
A
L
U
ACC
PC
IR
Varieties of processors
ALU | Arithmetic Logic Unit
PC | Program Counter
MAR | Memory Address Register
MDR | Memory Data Register
IR | Instruction Register
ACC | Accumulator
M
A
R
M
D
R
Memory

## Slide 10
Stack Machine
CPU
A
L
U
STACK
PC
IR
Varieties of processors
ALU | Arithmetic Logic Unit
PC | Program Counter
MAR | Memory Address Register
MDR | Memory Data Register
IR | Instruction Register
M
A
R
M
D
R
Memory

## Slide 11
Load/Store Machine
CPU
A
L
U
REGISTER
PC
IR
Varieties of processors
ALU | Arithmetic Logic Unit
PC | Program Counter
MAR | Memory Address Register
MDR | Memory Data Register
IR | Instruction Register
M
A
R
M
D
R
Memory
FILE

## Slide 12
Closer view of CPU - central processing unit
data path
  data registers such as ACC (accumulator) or set of general registers
  address registers such as SP (stack pointer) and Xn (index registers)
  ALU (arithmetic and logic unit) which executes operations
  internal buses (transfer paths)

## Slide 13
Closer view of CPU - central processing unit
memory bus interface / BIU (bus interface unit)
  MAR (memory address register) – a CPU register that either stores the memory address from which data will be fetched to the CPU or the address to which data will be sent and stored
  MDR (memory data register -- perhaps better called memory _buffer_ reg) – a CPU register that contains the data to be stored in memory or the data after a fetch from memory.

## Slide 14
Closer view of CPU - central processing unit
control
  PC (program counter) - points to next instruction (x86 calls it the IP == instruction pointer)
  IR (instruction register) - holds current instruction
  PSR (processor status register) - indicates results of previous operation (called condition codes or flags)

## Slide 15: closer view of CPU - central processing unit
PC (program counter)
IR (instruction register)
PSR (processor status register)
…
…
ACC
MAR (memory address register)
MDR (memory data register)
…
to and
from
memory
…
ALU
…
Move PC to MAR
read memory
. . .
Control signals to cause datapath actions
are generated by logic in the control unit

## Slide 16: fetch-execute cycle
each instruction generates a sequence of control signals (instruction fetch is the same for each instruction)
the control signals determine the register transfers in data path
timing - how long should the control signals be active? data signals must travel from a register, across the bus, through the ALU, to a register => minimum clock cycle time

## Slide 17: fetch-execute flowchart
fetch
decode
execute
load
execute
add
execute
store
+---+---------------+---------------------+---------- ...
...
...
+---+---------------+---------------------+---------- ...
like a switch statement –
decode selects
one of these execution paths
for A := B + C ;
assembly code / action on computer
;
load(B) ; ACC <- memory[B] register is loaded with a copy
; of the value in memory[B]
add(C) ; ACC <- ACC + memory[C] value in ACC register is added with
; a copy of the value in memory[C],
; and sum is placed in ACC register
store(A) ; memory[A] <- ACC memory[A] gets a copy of the value
; in ACC register

## Slide 18: register transfers (datapath actions) for these three instructions
---fetch---
---decode---
---execute---
get address
fetch operand
execute
store result
load
load(B)
MAR addr(IP)
READ
ACC MDR
_ _ _ _ _ _ _ _
MAR PC
READ
IR MDR
PC PC + incr
decode IR
+----------------------------+------------------------+
add(C)
MAR addr(IP)
READ
ACC ACC + MDR
_ _ _ _ _ _ _ _ _
store(A)
MAR addr(IP)
MDR ACC
_ _ _ _ _ _ _ _
WRITE
+--------------------------+----------------------------+
can check for external signals (interrupts) between instructions