## Slide 1
One goal of instruction set design is to minimize instruction length
Many instructions were designed with compilers in mind.
Determining how operands are addressed is a key component of instruction set design
Instruction Set Design
Notes: In a high level language, we do not (ordinarily) specify addressing modes. Instead, we just use variables and constants and rely on the language to know what we're talking about: if we use the constant 10 the compiler generates immediate mode; if we use the variable x the compiler generates direct mode.
The assembler doesn't work that way. At this level, the assembler is perfectly happy to use a constant 1 as a direct address, or to use the address of j as an immediate value. So we have to tell the assembler what we want to do.

## Slide 2
Defines the layout of bits in an instruction
Includes opcode and includes implicit or explicit operand(s)
Usually there are several instruction formats in an instruction set
Huge variety of instruction formats have been designed; they vary widely from processor to processor
Instruction Format
Notes: In a high level language, we do not (ordinarily) specify addressing modes. Instead, we just use variables and constants and rely on the language to know what we're talking about: if we use the constant 10 the compiler generates immediate mode; if we use the variable x the compiler generates direct mode.
The assembler doesn't work that way. At this level, the assembler is perfectly happy to use a constant 1 as a direct address, or to use the address of j as an immediate value. So we have to tell the assembler what we want to do.

## Slide 3
The most basic issue
Affected by and affects:
  Memory size
  Memory organization
  Bus structure
  CPU complexity
  CPU speed
Trade off between a powerful instruction repertoire and saving space with shorter instructions
Instruction Length
Notes: In a high level language, we do not (ordinarily) specify addressing modes. Instead, we just use variables and constants and rely on the language to know what we're talking about: if we use the constant 10 the compiler generates immediate mode; if we use the variable x the compiler generates direct mode.
The assembler doesn't work that way. At this level, the assembler is perfectly happy to use a constant 1 as a direct address, or to use the address of j as an immediate value. So we have to tell the assembler what we want to do.

## Slide 4
Large instruction set => small programs
Small instruction set => large programs
Large memory => longer instructions
Fixed length instructions same size or multiple of bus width => fast fetch
Variable length instructions may need extra bus cycles
Instruction format trade-offs
Notes: In a high level language, we do not (ordinarily) specify addressing modes. Instead, we just use variables and constants and rely on the language to know what we're talking about: if we use the constant 10 the compiler generates immediate mode; if we use the variable x the compiler generates direct mode.
The assembler doesn't work that way. At this level, the assembler is perfectly happy to use a constant 1 as a direct address, or to use the address of j as an immediate value. So we have to tell the assembler what we want to do.

## Slide 5
Processor may execute faster than fetch
  Use cache memory or use shorter instructions
Note complex relationship between word size, character size, instruction size and bus transfer width
  In almost all modern computers these are all multiples of 8 and related to each other by powers of 2
Instruction format trade-offs
Notes: In a high level language, we do not (ordinarily) specify addressing modes. Instead, we just use variables and constants and rely on the language to know what we're talking about: if we use the constant 10 the compiler generates immediate mode; if we use the variable x the compiler generates direct mode.
The assembler doesn't work that way. At this level, the assembler is perfectly happy to use a constant 1 as a direct address, or to use the address of j as an immediate value. So we have to tell the assembler what we want to do.

## Slide 6
Determines several important factors
Number of addressing modes
  Implicit operands don’t need bits
  X86 uses 2-bit mode field to specify Interpretation of 3-bit operand fields
Number of operands
  3 operand formats are rare
  For two operand instructions we can use one or two operand mode indicators
  X86 uses only one 2-bit indicator
Allocation of bits
Notes: In a high level language, we do not (ordinarily) specify addressing modes. Instead, we just use variables and constants and rely on the language to know what we're talking about: if we use the constant 10 the compiler generates immediate mode; if we use the variable x the compiler generates direct mode.
The assembler doesn't work that way. At this level, the assembler is perfectly happy to use a constant 1 as a direct address, or to use the address of j as an immediate value. So we have to tell the assembler what we want to do.

## Slide 7
Determines several important factors
Register versus memory
  Tradeoff between # of registers and program size
  Studies suggest optimal number between 8 and 32
  Most newer architectures have 32 or more
  X86 architecture allows some computation in memory
Allocation of bits
Notes: In a high level language, we do not (ordinarily) specify addressing modes. Instead, we just use variables and constants and rely on the language to know what we're talking about: if we use the constant 10 the compiler generates immediate mode; if we use the variable x the compiler generates direct mode.
The assembler doesn't work that way. At this level, the assembler is perfectly happy to use a constant 1 as a direct address, or to use the address of j as an immediate value. So we have to tell the assembler what we want to do.

## Slide 8
Determines several important factors (cont'd)
Number of register sets
  RISC architectures tend to have larger sets of uniform registers
  Small register sets require fewer opcode bits
  Specialized register sets can reduce opcode bits further by implicit reference (address vs. data registers)
Allocation of bits
Notes: In a high level language, we do not (ordinarily) specify addressing modes. Instead, we just use variables and constants and rely on the language to know what we're talking about: if we use the constant 10 the compiler generates immediate mode; if we use the variable x the compiler generates direct mode.
The assembler doesn't work that way. At this level, the assembler is perfectly happy to use a constant 1 as a direct address, or to use the address of j as an immediate value. So we have to tell the assembler what we want to do.

## Slide 9
Determines several important factors (cont’d)
Address range
  Large address space requires large instructions for direct addressing
  Many architectures have some restricted or short forms of displacement addressing
    Ex : x86 short jumps and loops,
    PowerPC 16-bit displacement addressing
Address granularity
  Size of object addressed
  Typically 8,16, 32 and 64 instruction variants
Allocation of bits

## Slide 10
For a given instruction set architecture, addressing modes define how machine language instructions identify the operand (or operands) of each instruction.
An addressing mode specifies how to calculate the effective memory address of an operand by using information held in registers and/or constants contained within a machine instruction or elsewhere.
Different types of addresses involve tradeoffs between instruction length, addressing flexibility, and complexity of address calculation
Addressing Modes

## Slide 11
Common addressing modes
  Immediate
  Direct
  Indirect
  Register
  Register indirect
  Displacement
  Implied (stack)
Addressing Modes

## Slide 12
the instruction itself contains the value to be used; located in the address field of the instruction; operand = address field.
e.g. add_immediate(5)
  add 5 to the contents of the accumulator
  5 is the operand
the value is stored in memory immediately after the instruction opcode in memory
Similar to using a constant in a high level language
Immediate Addressing

## Slide 13
Advantage
  fast, since the value is included in the instruction; no memory reference to fetch data
Disadvantage
  not flexible, since the value is fixed at compile-time
  can have limited range in machines with fixed length instructions
operand
Instruction
Immediate Addressing
opcode

## Slide 14
for the following example, assume an accumulator machine structure and that an add_immediate instruction is stored in memory, beginning at location 12
memory
assembly lang addr contents hardware actions
------------------- ------ ------------ -----------------------
... ...
add_immediate(5) 12 | 41 | acc acc + 5
13 | 5 |
... ... no additional memory
fetch for data beyond the
instruction fetch (since
the instruction contains
the data being used)
since an add must have different hardware actions than an add_immediate, add_immediate has to be a different opcode (or there has to be an extra type-of-addressing-mode code in the instruction format to go along with the opcode)
Immediate Addressing

## Slide 15
Direct Addressing
The instruction tells where the value can be found, but the value itself is out in memory.
The address field contains the address of the operand
Effective address (EA) = address field (A)
  e.g. add(A)
    Add contents of memory address A to the accumulator
    Look in memory at address A for operand
  In a high level language, direct addressing is frequently used for things like global variables.

## Slide 16
Direct Addressing
Advantage
  Single memory reference to access data
  No additional calculations to determine effective address
  More flexible than immediate
Disadvantage
  Limited address space

## Slide 17: Direct Addressing
Address A
Opcode
Instruction
Memory
Operand
Notes: 6

## Slide 18: Direct Addressing for the following example, assume an accumulator machine structure and that an add instruction is stored in memory, beginning at location 12 memory assembly lang addr contents hardware actions ------------------- ------ ------------ ----------------------- ... ... add(one) 12 | 40 | acc acc + memory[24] 13 | 24 | = acc + 1 ... ... word(one,1) 24 | 1 | effective address = 24 ... ... so, when the PC points to 12: 40 (i.e., the contents of location 12) is interpreted as an opcode 24 (i.e., the contents of location 13) is interpreted as an address 1 (i.e., the contents of location 24) is interpreted as data note that there are no tags or other indicators that the number 40 in location 12 has to be an opcode; it could just as well be used as an address or as data

## Slide 19
Suppose we have a statement in C like
  b = a + 10;
a and b are variables, so they are out in memory.
To execute this statement, we will need to fetch a from memory, and write our result to b.
That means the instructions we generate need to have the addresses of a and b, and need to read and write those addresses as appropriate.
The number 10 is an actual value appearing in the statement. So, our code needs to include 10 itself.
Example of Immediate and Direct Addressing Modes

## Slide 20
The memory cell pointed to by the address field contains the address of (pointer to) the operand
EA = (A)
  Look in A, find address in A and look there for the operand
e.g. add_indirect(A)
  add contents of memory cell pointed to by contents of A to accumulator
Memory-Indirect Addressing

## Slide 21
Memory-Indirect Addressing
Advantages:
  Large address space
  2n where n = word length
  May be nested, multilevel, cascaded
Disadvantage
  Multiple memory accesses; hence, slower

## Slide 22: Indirect Addressing
Address A
Opcode
Instruction
Memory
Operand
Pointer to operand
Notes: 9

## Slide 23
for the following example, assume an accumulator machine structure and that an add instruction is stored in memory, beginning at location 12
memory
assembly lang addr contents hardware actions
------------------- ------ ----------- -----------------------
... ...
add_indirect(ptr) 12 | 42 | acc acc + memory[memory[36]]
13 | 36 | = acc + memory[24]
... ...
word(one,1) 24 | 1 | = acc + 1
... ...
word(ptr,one) 36 | 24 | effective address = 24
... ...
the address included in the instruction is that of a pointer, that is, a word that holds another address
Indirect Addressing

## Slide 24: Register Addressing
Operand is held in register named in address field
EA = R
Advantages
No memory accesses
Very fast execution
Very small address field needed
  Shorter instructions
  Faster instruction fetch
Notes: 10

## Slide 25: Register Addressing
Advantages (cont'd)
Multiple registers improve performance
Note: in C you can specify register variables
    register int a;
  This is only advisory to the compiler; no guarantees
Disadvantage
  Limited number of registers
Notes: 10

## Slide 26: Register Addressing
Register Address R
Opcode
Instruction
Registers
Operand
Notes: 12

## Slide 27: Register Indirect Addressing
Similar to indirect addressing
EA = (R)
Operand is in memory cell pointed to by contents of register R
Large address space (2n)
One fewer memory access than indirect addressing
Notes: 13

## Slide 28: Register Indirect Addressing Diagram
Register Address R
Opcode
Instruction
Memory
Operand
Pointer to Operand
Registers
Notes: 14

## Slide 29: Displacement Addressing
EA = A + (R)
Address field hold two values
  A = base value
  R = register that holds displacement
  or vice versa
Notes: 15

## Slide 30: Displacement Addressing
Register R
Opcode
Instruction
Memory
Operand
Pointer to Operand
Registers
Address A
+
Notes: 16

## Slide 31: Relative Addressing
A version of displacement addressing
R = Program counter, PC
EA = A + (PC)
i.e. get operand from A cells from current location pointed to by PC
Notes: 17

## Slide 32: Base-Register Addressing
A holds displacement
R holds pointer to base address
R may be explicit or implicit
Notes: 18

## Slide 33: Indexed Addressing
A = base
R = displacement
EA = A + R
Good for accessing arrays
  EA = A + R
  R++
Notes: 19

## Slide 34: Combinations
Postindex
EA = (A) + (R)
Preindex
EA = (A+(R))
Notes: 20

## Slide 35: Stack Addressing
Operand is (implicitly) on top of stack
e.g.
  ADD Pop top two items from stack and add
Notes: 21