## Slide 1: Control Structures in ARM
Implementation of Decisions
Similar to accumulator instructions
One instruction sets the flags, followed by another instruction that uses the flags to make the actual branch decision
ARM compare and test instructions set the flags
Instruction | Operation | Notes
cmp rn, <op2> cmn rn, <op2> | rn - <op2> rn += <op2> | Always updates NZCV
tst rn, <op2> teq rn, <op2> | rn & <op2> rn ^ <op2> | Always updates NZ, if shifted. <op2> may affect C flag

## Slide 2: Conditional Execution
Conditional instructions make a decision to execute based on the state of the appropriate flag. The condition is specified with a two-letter suffix
Suffix | Description | Flags tested
eq | Equal | Z = 1
ne | Not equal | Z = 0
cs / hs | Unsigned higher or same | C = 1
cc / lo | Unsigned lower | C = 0
mi | Minus | N = 1
pl | Positive or Zero | N = 0
vs | Overflow | V = 1
vc | No overflow | V = 0
hi | Unsigned higher | C = 1 & Z = 0
ls | Unsigned lower or same | C = 0 or Z = 1
ge | Greater than or equal | N = V
lt | Less than | N != V
gt | Greater than | Z = 0 & N = V
le | Less than or equal | Z = 1 or N = !V
al | Always | 
Notes: Condition codes are simply a way of testing the ALU status flags.
This slide is for reference only.

## Slide 3: Conditional Execution
The two-letter suffix should be used in conjunction with other instructions. For examples:
beq
bge
addlt
subgt
Using a two-letter suffix as a stand-alone instruction is meaningless and will cause a syntax error.
Notes: Condition codes are simply a way of testing the ALU status flags.
This slide is for reference only.

## Slide 4: ARM Branch Instructions
Unconditional branch
  B (or BAL) branch always
Conditional branches
testing result of compare or other operation (signed arithmetic):
  beq – branch on equal (Z==1)
  bne – branch on not equal (Z==0)
  bls – branch on less than ((N xor V)==1)
  ble – branch on less than or equal ((Z or (N xor V))==1)
  bge – branch on greater than or equal ((N xor V)==0)
  bgt – branch on greater than ((Z or (N xor V))==0)

## Slide 5: C if statement in ARM
  int x;
  int y;
  if(x == 0)
  y = 1;
  /* assume x is in r0, y is in r1 */
exit
x == 0?
y = 1
(false)
(true) x == 0
C Source Code | Ineffficient Assembly | Efficient Assembly
int x; int y; if(x == 0) y = 1; | cmp r0, #0 beq then b endif then: mov r1, #1 // now store r1 in [y] endif: . . . | cmp r0, #0 bne endif then: mov r1, #1 // now store r1 in [y] endif: . . .

## Slide 6: C if statement in ARM
  Note that the "Inefficient Assembly" code contains back-to-back branches (beq followed by b). We would like to avoid this, since branches may cause a delay slot.
  One way to remove the back-to-back branches is to change the condition for branching, as in the "Efficient Assemble" code.
C Source Code | Ineffficient Assembly | Efficient Assembly
int x; int y; if(x == 0) y = 1; | cmp r0, #0 beq then b endif then: mov r1, #1 // now store r1 in [y] endif: . . . | cmp r0, #0 bne endif then: mov r1, #1 // now store r1 in [y] endif: . . .

## Slide 7: C if statement in ARM
  if((x+b)>z)
    x+=y;
ARM code:
/* assume x is in r0
y is in r1, and z is in r2
*/
add r3, r0, r1
cmp r3, r2
ble false // branch to false when((x+y)>z)
// is false
add r0, r0, r1 // x = x+y
/* now store content of r0 to [x] */ false:
exit
x+y > z?
x += y
(false)
(true) (x+y)>z

## Slide 8: C if-else statement in ARM
if(i == j)
f=g+h;
else
f=g-h;
ARM code:
/* assume f is in r0, i is in r1,
j is in r2, g is in r3, h is in r4,
*/
cmp r1, r2 // Z = 1 if i==j
beq true // branch to true when i==j sub r0, r3, r4 // f = g-h (false) b done // branch to done true: add r0, r3,r4 // f = g+h (true) done:
exit
i == j?
f=g+h
f=g-h
(false) i != j
(true) i == j

## Slide 9: Conditional execution in ARM
An unusual ARM feature is that all instructions may be conditional:
  CMP r0, #5 // if (r0 != 5)
  {
  ADDNE r1, r1, r0 // r1 := r1 + r0 - r2
  SUBNE r1, r1, r2
  }
this removes the need for some short branches, improving performance and code density

## Slide 10: ARM Control Structures
Implementing Loops
All for loops, while loops, and do-while loops have an implicit branch from the bottom to the top of the loop.
This branch instruction becomes explicit when translated into assembly.
while loop /* assume x is in r0
while ( x <= 10 ) and y is in r1 */
{ loop:
x = x + y; cmp r0, #10 // test condition
} bgt done
add r0, r0, r1
b loop
done:

## Slide 11: Loops in C/Assembly
for loop // x: r0, y: r1, z: r2
for ( x = 1; x <= y; x++ ) mov r0, #1
{ loop:
z *= x; cmp r0, r1 // test condition
} bgt done
mul r2, r2, r0
rewritten as while loop add r0, r0, #1
x = 1; b loop
while ( x <= y ) done:
{
z *= x;
x++;
}

## Slide 12: Control Structures in ARM
for loop, counted up from 0 to n-1 /* i : r0, n: r1 */
for ( i = 0; i < n; i++ ) {
<body> mov i, #0 //clear itest:
} loop:
cmp r0, r1
rewritten as while loop bge done
i = 0; <body>
while ( i < n ) add r0, r0, #1
{ b loop
<body> done:
i++;
}

## Slide 13: Control Structures in ARM
for loop, counted up from 1 to n i .req r0
for ( i = 1; i <= n; i++ ) { n .req r1
<body> mov r1, #1
} loop:
cmp i, n
bgt done
rewritten as while loop <body>
i = 1; add i, i, #1
while(i <= n) b loop
{ done:
<body>
i++;
}

## Slide 14: Control Structures in ARM
for loop, counted down from to n to 1
for ( i = n; i > 0; i-- ) i .req r0
{ n .req r1
<body> mov n, i
} loop:
cmp i, #0
ble done
rewritten as while loop <body>
i = n; sub i, i, #1
while ( i > 0 ) b loop
{ done:
<body>
i--;
}