## Slide 1: What is the Internet?
CPSC 3600

## Slide 2: What networking challenges were described in the assigned article?
Notes: https://developer.oculus.com/blog/networked-physics-in-virtual-reality-networking-a-stack-of-cubes-with-unity-and-physx/

## Slide 3: Learning Objectives
Covering Sections 1.1 - 1.3 today
Introduction to terminology and concepts that will be expanded later in the course
Big picture overview of the physical structure of networks

## Slide 4: What is the Internet?

## Slide 5: What is the Internet?
The hardware, standards, and services required to create a massively interconnected network of devices

## Slide 6: Hardware
End systems/Hosts
  PCs, laptops, servers, phones, toasters, ...
Communication links
  Fiber, copper, radio, satellite, …
Packet switches + routers
  (e.g. traffic lights, street signs, traffic cops, …)

## Slide 7: Hardware - Traffic analogy
End systems/Hosts
  Houses, stores, warehouses, hospitals, ...
Communication links
  Interstates, highways, roads, driveways, ...
Packet switches + routers
  Traffic lights, street signs, traffic cops, …
Notes: Packets are cars carrying people and goods
Hosts and end systems are the places people are, or where they want to be. Edge nodes on the network
Communication links are the connections that allow people to move from one place to another. Just like roads, links have different capacities
  Transmission rate/bandwidth → theoretical # of cars per hour → # of lanes * speed limit
  Throughput ~ actual # of cars per hour → bandwidth + reality (jams, crashes, etc)
  Driveway is like your connection to your ISP, it’s what provides you with initial access to the road network
  Just like roads all over the earth, most parts of the Internet are interconnected to each other
  The “darknet” is just parts of the internet that are more difficult to access (e.g. require off roading to get to)
Packet switches and routers are the infrastructure that connects roads together and helps drivers figure out what path to take

## Slide 8: Standards
Need standards to facilitate communication between interconnected devices
  E.g. Drive on the right side of the road, stop at red octagons, …
Many different protocols control sending and receiving of different messages
  TCP, IP, HTTP, Skype, 802.11, …
Defined by different entities IETF and RFC
  IETF: Internet Engineering Task Force
  RFC: Request for comments

## Slide 9: Protocols
Protocols define:
  The format of a message
  The order of messages sent and received
  The actions taken on transmitting or receiving a message
All communication on the Internet is governed by protocols
  Transmission Control Protocol (TCP)
    Protocol to enable reliable communication between end systems
  Internet Protocol (IP)
    Protocol to communicate between routers and end systems

## Slide 10: Protocols
Human Protocol Computer Protocol

## Slide 11: Services
Infrastructure that provides services to applications
  The Web, VoIP, email, games, e-commerce, …
Provides programming interface to applications
  Hooks that allow sending and receiving to other programs
  Provides services, analogous to postal service forwarding

## Slide 12: Class Activity (~5 minutes)
Pair up with a neighbor and explain the role of Hardware, Standards/Protocols, and Services with regard to the Internet, and how they can be fit into the traffic analogy

## Slide 13: Network Edge and Core
The types of hardware used in the Internet map onto another way of describing it
  The Edge: clients, servers (places where apps and data are)
  The Core: interconnected routers

## Slide 14: Network Edge
Essentially any device you use is an Edge device
  End systems, hosts
Edge router is the first router an edge device
Many ways to connect to an edge router
  Residential access nets
  Institutional access networks (school, company)
  Mobile access networks
Differences?
  Bandwidth, shared/dedicated, download/upload, ...

## Slide 15: Home Access: DSL (Digital Subscriber Line)
Shares existing phone line, voice split from data
< 24 Mbps download, < 2.5 Mbps upload (asymmetric)

## Slide 16: Home Access: DSL (Digital Subscriber Line)
Shares a single line by using different frequencies for different types of data
  High-speed download in 50 kHz to 1 MHz band
  Medium-speed upload in 4 kHz to 50 kHz band
  Voice in 0 to 4 kHz band
DSL design for 5 to 10 mile connections to central office
  Distance affects transmission over physical medium used (twisted-pair cables)

## Slide 17: Home Access: Cable
Uses existing cable TV infrastructure
< 100 Mbps download, < 10 Mbps upload (asymmetric)
Transmission medium: hybrid fiber coax (HFC)

## Slide 18: Home Access: Cable
Shared cables between homes connecting to cable head end, unlike DSL which has dedicated lines
  Every packet sent by head end travels to every connected home
  Activity of other homes can affect your bandwidth

## Slide 19: Home Access: Cable
Accomplished via frequency division multiplexing

## Slide 20: Enterprise Access: LAN (Local Area Network)
More devices than home systems, greater internal complexity for the institutional network
Supports very high transmission rates (10 Gbps+)

## Slide 21: Home/Enterprise Access: WiFi
Shared wireless access network connects end system to router (potentially via an access point / base station)
Wireless LAN
  Range of ~100ft
  802.1 b/g/n/ac protocols, different transmission rates
    11 Mbps, 54 Mbps, 450 Mbps, 1.3 Gbps
  WiFi cards, routers support specific set of protocols

## Slide 22: Wide-area Wireless
Different technology for wide-area networks (e.g. phones)
Range of 10+ km from cellular tower
Transmission speeds between 1 and 10 Mbps
Different protocols
  3G, 4G, 4G LTE, ...

## Slide 23: Physical Media
Several different types of “physical media” used to establish network connections
  Twisted-pair copper wire
  Coaxial cable
  Fiber optics
  Radio (Terrestrial/Satellite)

## Slide 24: Twisted-pair Copper Wire
Least expensive, most commonly used medium
Two insulated copper wires twisted around each other
  Twisting reduces electrical interference from other nearby pairs
Many pairs can be twisted together into a single cable
Data rates range between 10 Mbps and 10 Gbps
  Length of cable negatively affects data rate
  Cables can be 100+ feet long
Ethernet cables are twisted-pair cables

## Slide 25: Coaxial Cable
Two copper wires, but not twisted. Instead, one is inside of the other, separated by insulation
Commonly used for cable connections
Carry multiple signals simultaneously on different frequencies

## Slide 26: Fiber Optics
Glass fiber carries light pulses, each one a bit of data
  Light constrained by total internal reflections
High-speed transmission (10 Gbps to 10+ Tbps)
  Travels at speed of light in glass (~200,000 km/s)
Low error rates
  Immune to electromagnetic noise
  Very low signal attenuation (up to 100 km)
Higher cost (including infrastructure)
  E.g. transmitters, switches, receivers, ...

## Slide 27: Radio
“Unguided” medium, signal carried in electromagnetic spectrum
Potential issues include reflection, interference, obstruction
Terrestrial microwave (45 Mbps channel)
WiFi (11 Mbps to 1.3 Gbps+)
Wide-area cellular (10+ Gpbs)
Satellite (kbps to 45 Mbps channel, high latency)
  Geostationary vs. low orbit (vs. interplanetary)

## Slide 28: The Network Core
Mesh of interconnected routers
Packet-switched network
  Hosts break data into individual packets
  Routers forward packets to next router along way to destination, till destination

## Slide 29: Host: Send Packets of Data
Application creates message
Message broken into packets of length L bits
Transmitted into the network at transmission rate R
  The link capacity, aka bandwidth

## Slide 30: Terminology
Mbps vs. MBps
  Lowercase b = bits
  Uppercase B = bytes
8 Mbps = 1 MBps
For this course, we will assume
  1 Kb = 1000 bits
  1 Mb = 1000 Kb
  1 Gb = 1000 Mb
  ...

## Slide 31: Packet Switching: Store and Forward
Packet switch waits till it has received the whole packet to begin sending to the next destination
  Why?
Two important implications
  Adds to transmission latency
  Have to store packets as they come in (memory buffer)

## Slide 32
Ignoring propagation delay, how long does it take for packet 1 to get to the destination?
1 L/R
2 L/R
3 L/R
4 L/R

## Slide 33
Ignoring propagation delay, how long does it take for packet 3 to get to the destination?
1 L/R
2 L/R
3 L/R
4 L/R

## Slide 34
Ignoring propagation delay, how long does it take for packet 1 to get to the destination if we have N total links?
1 L/R
N * L/R
2N * L/R
N2 * L/R

## Slide 35
Ignoring propagation delay, how long does it take for packet 3 to get to the destination if we have N total links?
N * L/R + 0 L/R
N * L/R + 1 L/R
N * L/R + 2 L/R
N * L/R + 3 L/R

## Slide 36: Packet Switching: Store and Forward
General solution for transmission time
  P packets of L bytes
  N routers with transmission rate R

## Slide 37: Packet Switching: Store and Forward
General solution for transmission time
  P packets of L bytes
  N links with transmission rate R
Transmission delay = N*L/R + (P-1)*L/R

## Slide 38: Packet Switching: Queuing delay, loss
If the arrival bit rate exceeds the transmission rate, then we have to buffer packets
  Adds latency as packets wait in the queue
  Packets can be dropped (lost) if the memory buffer fills up

## Slide 39: Packet Switching: Routing Packets
In a packet switched network, the router has to decide which is the next router it should send a packet to
  Routing: determines source-destination route taken by packets
Routing can be done differently in different systems

## Slide 40: Packet Switching: IP Routing
The Internet uses IP addresses for routing
  E.g. 104.62.113.162, or 192.168.1.12
Routers contain forwarding tables that map different outbound links to different destination addresses
Notes: www.traceroute.org

## Slide 41: Circuit Switching
Alternative to packet switching
Reserves an end-to-end pipeline between source and destination
  No sharing with other users
  Ensures you get full access
  Resources will be wasted when you are idle
Used for traditional telephone networks

## Slide 43: Circuit Switching: Multiplexing
In practice, doesn’t need dedicated hardware, just dedicated resources
Two options
  Frequency domain multiplexing (e.g. radio stations)
  Time domain multiplexing

## Slide 45: Packet Switching vs. Circuit Switching
Each have advantages, disadvantages, however most systems today use packet switching
Under most circumstances, packet switching will result in better utilization of resources by more users

## Slide 46
Assume each user
  Uses 100 kb/s when “active”
  Active for 10% of the time

## Slide 47
Assume each user
  Uses 100 kb/s when “active”
  Active for 10% of the time
How many users can circuit switching support?

## Slide 48
Assume each user
  Uses 100 kb/s when “active”
  Active for 10% of the time
How many users can circuit switching support?
What is the average utilization of the link?

## Slide 49
Assume each user
  Uses 100 kb/s when “active”
  Active for 10% of the time
How many users can packet switching support?
  No simple answer, probabilistic
  Can compute using binomial distribution

## Slide 50
Easily supports 35 users
  p>10 users = 0.0004
  p<10 users = 0.9982

## Slide 51
Easily supports 35 users
  p>10 users = 0.0004
  p<10 users = 0.9982
What happens during the 0.04% of the time when > 10 users are active simultaneously?

## Slide 52
What happens if we have 150 users?
  p>10 users = 0.8986
  p<10 users = 0.0600
What effect will this have on the buffer?

## Slide 53: Packet Switching vs. Circuit Switching
Packet switching is great for bursty data, where users aren’t constantly transmitting
  Easier to share resources
  No need to setup/tear down a circuit
Possible to get excessive congestion that prevents anyone from using the network
  Need protocols to handle congestion, ensure reliable data transmission
Unsolved problem how to guarantee bandwidth for audio/video apps using packet switched networks

## Slide 54: Structure of the Internet
The internet is a network of networks (of networks...)
  End systems connect to Internet via an access ISP (internet service provider)
  Access ISPs have to be interconnected to enable communication
  Resulting networks evolved organically over time, driven by economics and national policies

## Slide 55
Given millions of access ISPs, how do you connect them?

## Slide 56
Fully interconnected??

## Slide 57
Connect through one global ISP?

## Slide 58
If one global ISP is a viable business, there will be competition

## Slide 59
So we need to connect the global ISPs

## Slide 60
Regional networks may arise to connect access nets to ISPs

## Slide 61
Major content providers may run their own networks to bring services close to users

## Slide 62: Before Next Class
Read Sections 1.4 (including all sub-sections)
Complete 3 of the following problems
  R1, R3, R5, R8, R11, R14
  Random students will be asked to share your answers to these problems at the start of the next class