## Slide 1: Protocol Layers
CPSC 3600

## Slide 2
R16: Consider sending a packet from a source host to a destination host over a fixed route. List the delay components in the end-to-end delay. Which of these delays are constant and which are variable?
R18: How long does it take a packet of length 1,000 bytes to propagate over a link of distance 2,500 km, propagation speed 2.5 *10^8 m/s, and a transmission rate of 2 Mbps? More generally, how long does it take a packet of length L to propagate over a link of distance d, propagation speed s, and transmission rate R bps? Does this delay depend on packet length? Does this delay depending on transmission rate?
R19: Suppose Host A wants to send a large file to Host B. The path from Host A to Host B has three links, of rates R1 = 500 kbps, R2 = 2 Mbps, and R3 = 1 Mbps
a) Assuming no other traffic in the network, what is the throughput for the file transfer?
b) Suppose the file is 4 million bytes. Dividing the file size by the throughput, roughly how long will it take to transfer the file to Host B?
c) Repeat a) and b), but now with R2 reduced to 100 kbps

## Slide 3
P6: This elementary problem begins to explore propagation delay and transmission delay, two central concepts in data networking. Consider two hosts, A and B, connected by a single link of rate R bps. Suppose that the two hosts are separated by m meters, and suppose the propagation speed along the link is s meters/sec. Host A is to send a packet of size L bits to Host B.
a) Express the propagation delay, d_prop in terms of m and s.
b) Determine the transmission time of the packet d_trans in terms of L and R.
c) Ignoring processing and queuing delays, obtain an expression for the end-to-end delay
d) Suppose Host A begins to transmit the packet at time t = 0. At time t = d_trans, where is the last bit of the packet?
e) Suppose d_prop is greater than d_trans. At time t = d_trans, where is the first bit of the packet?
f) Suppose d_prop is less than d_trans. At time t = d_trans, where is the first bit of the packet?
g) Suppose s = 2.5*10^8, L=120 bits, and R = 56 kbps. Find the distance m so that d_prop = d_trans.

## Slide 4
P7: In this problem, we consider sending real-time voice from Host A to Host B over a packet-switched network (VoIP), Host A converts analog voice to a digital 63 kbps bit stream on the fly. Host A then groups the bits into 56-byte packets. There is one link between Hosts A and B; its transmission rate is 2 Mbps and its propagation delay is 10 msec. As soon as Host A gathers a packet, it sends it to Host B. As soon as Host B receives an entire packet, it converts the packet's bits to an analog signal. How much time elapses from the time a bit is created (from the original analog signal at Host A) until the bit is decoded (as part of the analog signal at Host B)
P12: A packet switch receives a packet and determines the outbound link to which the packet should be forwarded. When the packet arrives, one other packet is halfway done being transmitted on this outbound link and four other packets are waiting to be transmitted. Packets are transmitted in order of arrival. Suppose all packets are 1,500 bytes and the link rate is 2 Mbps. What is the queuing delay for the packet? More generally, what is the queuing delay when all packets have length L, tranmission rate R, x bits of the currently-being transmitted packet have been transmitted, and n packet are already in the queue.

## Slide 5
P20: Consider the throughput example corresponding to Figure 1.20(b). Now suppose that there are M client-server pairs rather than 10. Denote Rs, Rc, and R for the rates of the server links, client links, and network link. Assume all other links have abundant capacity and that there is no other traffic in the network besides the traffic generated by the M client-server pairs. Derive a general expression for throughput in terms of Rs, Rc, R, and M.

## Slide 6: Protocol Layers
Networks are complex, with many pieces
  Hosts
  Routers
  Different types of links
  Applications
  Protocols
  Hardware/software
To help manage this complexity, network protocols are implemented in several layers
  Each layer only has to talk to the layer above it and below it

## Slide 7: Analogy: Airline Travel

## Slide 8: Analogy: Airline Travel
Each layer implements a service
  Via its own internal-layer actions
  Relying on services provided by layer below it
  Using data from the layer above it

## Slide 9: Why layering?
Explicit structure allows identification, relationship of complex system pieces
  Layered reference model for discussion
Modularization eases maintenance, updating of system
  Changing implementation of a layer is transparent to the system
  E.g. Changing gate procedure doesn’t affect anything else

## Slide 10: Internet Protocol Stack
Five layers in the Internet’s protocol stack
  Application: supports network applications
    e.g. FTP, SMTP, HTTP
  Transport: process-process data transfer
    e.g. TCP, UDP
  Network: routing of packets from source to destination
    e.g. IP, routing protocols
  Link: data transfer between neighboring network elements
    e.g. Ethernet, 802.1, PPP
  Physical: bits “on the wire”

## Slide 11
Application Layer
Transport Layer
Network Layer
Link Layer
Physical Layer
Application Layer
Transport Layer
Network Layer
Link Layer
Physical Layer
“Talks to” destination transport layer
“Talks to” other network layers
“Talks to” the next link layer
Actually “talks”
Ports
IP Addresses
MAC Addresses

## Slide 12
Application Layer
Transport Layer
Network Layer
Link Layer
Physical Layer
Application Layer
Transport Layer
Network Layer
Link Layer
Physical Layer
Socket API
Creates the data to be sent
Provides services, basic routing (ports)
Bits moving across physical medium
Injects bits onto the physical medium
Keeps routing tables up to date Forwards incoming packets to outgoing link
Handles logistics of communication across the adjacent link

## Slide 13: ISO/OSI Reference Model
Adds two additional layers
  Presentation: allow applications to interpret meaning of data, e.g. encryption, compression, machine-specific conventions
  Session: synchronization, checkpointing, recovery of data exchange
Internet stack doesn’t have these layers, if these services are needed they must be implemented in the application

## Slide 14: Encapsulation
Each layer has to add additional information to a packet, related to that layer’s function
  This information is appended to the packet (encapsulated)
  This information is then extracted and used the next time that packet is processed by another layer of the same type
See more detail later about what is added by each layer

## Slide 16: Application Layer
Standardizes protocols used when communicating between processes on separate hosts
  HyperText Transfer protocol (HTTP)
  File Transfer protocol (FTP)
  Simple Mail Transfer protocol (SMTP)
  Domain Name System (DNS)
Anyone can create their own standards that reside in the “application” layer
Responsible for creating the payload of a packet

## Slide 17
Find other application/network protocols besides HTTP, FTP, SMTP, DNS

## Slide 18: Transport Layer
Moves packets from host application to destination application
Transport layer packets referred to as segments
Two transport protocols for the Internet
  UDP: connectionless service, no reliability, flow/congestion control
  TCP: connection-oriented service, guarantees packets will be delivered correctly, handles flow/congestion control
Transport layer is where many essential services are implemented

## Slide 19: Transport Services
Four major classes of services that can be offered
  Reliable data transfer
  Throughput
  Timing
  Security
Important to remember: we’re focusing on the Internet, one specific type of network that can be implemented
  The Internet’s transport layer does not implement all of these services

## Slide 20: Reliable Data Transfer Services
Packets can get lost when crossing a link
  Queue overflow leads to dropped packets
  Bits get corrupted due to interference/noise
This is OK for some applications (e.g. streaming video), but devastating for others (e.g. financial applications, email)
Reliable data transfer guarantees packets will be delivered successfully (or you’ll know if they weren’t)

## Slide 21: Throughput Services
Some applications need a guaranteed amount of throughput to be useful (e.g. VoIP application)
  Beneficial if this throughput could be guaranteed, (similar to a circuit switched network)

## Slide 22: Timing Services
Other applications would benefit from guarantees about how long it will take to deliver a packet (e.g. multiplayer video games)
  Timing services would attempt to ensure delivery within the specified window

## Slide 23: Security Services
Many different possible security services
  Encrypt the data stream, ensure no one can read it except recipient
  Ensure data integrity, no one has tampered with the data
  Authenticate the end-point, make sure the recipient is who you think they are

## Slide 24: TCP Service
TCP includes a reliable transfer service, can include security features with SSL
Also provides basic error checking, congestion control mechanism, flow control

## Slide 25: UDP Service
UDP only provides basic error checking, no other guarantees
Faster (ignoring congestion), more lightweight than TCP

## Slide 28
What is a network port, and why is it important?

## Slide 29: Network Layer
Routes segments from their source to their destination
Network layer packets referred to as datagrams
Two major functions
  Routing
  Forwarding

## Slide 30: Routing
Routing keeps the routers knowledge of downstream destinations up to date
  Maintains the forwarding table by communicating with other routers
  Looks for network outages so as to reroute packets
  Periodic process, takes seconds to complete

## Slide 31: Forwarding
Forwarding determines which output link an incoming packet should be transmitted on
Accomplished using the forwarding table created during by the routing function

## Slide 33: Link Layer
Moves datagrams from one network element to the next
Link layer packets referred to as frames
Only deals with the link between two routers/switches
Examples of protocols include Ethernet, WIFI, DOCSIS
  Possible for a packet to cross several links using different protocols before it reaches its destination
Lives in the network interface card

## Slide 35: Physical Layer
Moves individual bits of a frame from one node to the next
Hardware-level features required to transmit bits across the used physical media
Protocols here depend on the protocol used in the link AND on the physical medium the link is made of
  E.g. different protocols for Ethernet when using twisted-pair cable vs. coaxial vs. fiber

## Slide 36
Application Layer
Transport Layer
Network Layer
Link Layer
Physical Layer
Application Layer
Transport Layer
Network Layer
Link Layer
Physical Layer
“Talks to” destination transport layer
“Talks to” other network layers
“Talks to” the next link layer
Actually “talks”
Ports
IP Addresses
MAC Addresses

## Slide 37
Application Layer
Transport Layer
Network Layer
Link Layer
Physical Layer
Application Layer
Transport Layer
Network Layer
Link Layer
Physical Layer
Socket API
Creates the data to be sent
Provides services, basic routing (ports)
Bits moving across physical medium
Injects bits onto the physical medium
Keeps routing tables up to date Forwards incoming packets to outgoing link
Handles logistics of communication across the adjacent link

## Slide 38
Explain the five layers used in the Internet model to your neighbor
What are the layers?
What services do they provide?
What header information do they add to a packet (encapsulation)

## Slide 39
Name one of the five layers in the Internet’s layered model.

## Slide 40
Which layer is responsible for routing packets to their destination?
Application Layer
Link Layer
Network Layer
Physical Layer
Transport Layer

## Slide 41
Which layer can provide the following services: reliable data transfer, throughput guarantees, timing guarantees?
Application Layer
Link Layer
Network Layer
Physical Layer
Transport Layer

## Slide 42
Which layer appends source/destination MAC addresses to the packet?
Application Layer
Link Layer
Network Layer
Physical Layer
Transport Layer

## Slide 43
Which layer appends source/destination ports to the packet?
Application Layer
Link Layer
Network Layer
Physical Layer
Transport Layer

## Slide 44: Before Next Class
Read Section 2.1, 2.5
Complete the first Wireshark Lab